## Slide 1
Shrewsbury Pi Meetup
Raspberry Pi ClusterHAT
Brian Lingard
Sept. 26, 2017

## Slide 2
What’s a cluster?
Computer cluster
  Group of networked computers where each node works on the same task
  HW is typically high performance or specially designed
  Think “supercomputer”
    i.e. thousands of nodes

## Slide 3
Internet
Basic Cluster Architecture
Host Node
Compute
Node 1
High Speed Network Switch
Compute
Node 2
Compute
Node 3
Compute
Node N
. . .
Storage Array

## Slide 4
What’s a cluster?
Beowulf cluster
  Name came from project built in 1994 by a pair of NASA engineers
  Group of commodity-grade computers connected in a network
  Repurposed older/low-end computers
  And now Raspberry Pi’s

## Slide 5
Raspberry Pi Clusters
Simple, home built
Usually 4 or 5 nodes
USB for power
Ethernet for comms
  Via switch

## Slide 6
Raspberry Pi Clusters
University projects
Usually 10 to 100 nodes

## Slide 7
Raspberry Pi Clusters
Specially designed I/O board
Custom designed for Pi-Zeros

## Slide 8
Pi Cluster Hat
Designed and built by 8086 Consultancy
HAT module plugs into Raspberry Pi A+/B+/2/3
Accepts up to 4 Pi Zero boards
Supplies power to each node
  Controlled via GPIO pins
Enables network comms
  Via USB gadget mode

## Slide 9
Pi Cluster Hat - Kit
Runs about $35
Kit comes with
  Cluster Hat board
  USB power cable
  Four stand-offs with screws

## Slide 10
Pi Zero W (an aside)
Only $10
1 Ghz, Single Core
512 MB RAM
Built-in WiFi, BT4.1 and BLE
CSI camera connector
Recommend using 4GB or 8GB SDcard
Mini
HDMI
USB
OTG
Micro
SD

## Slide 11
Pi Cluster Hat – Full Setup
Still compact when fully configured
Gets power from Raspberry Pi host
Pi Zeros get comms and power via USB
Recommend using 16GB or 32GB SDcard

## Slide 12
Ethernet
LAN
Pi Cluster Hat Architecture (ver 1.x)
Raspberry
Pi 3
(Host)
Pi
Zero
1
USB Networking
Power / GPIOs
USB4
USB3
USB2
USB1
GPIO22
GPIO23
GPIO24
GPIO25
Pi
Zero
2
Pi
Zero
3
Pi
Zero
4
HDMI
Monitor
USB
Keyboard/Mouse

## Slide 13
Pi Cluster Hat – Software Setup
See https://clusterhat.com/setup-software
Configure Raspberry Pi host using
  PIXEL controller image
    Standard Raspbian with extras
Configure each Pi Zero W node using
  LITE image (host names set to P1, P2, etc)
    No GUI
  Setup password-less ssh
  Optionally setup WiFi on each Pi Zero W

## Slide 14
Pi Cluster Hat – Useful Packages
Distribute
  https://github.com/PaulBrownMagic/ClusterHat_Distribute
MPICH
  sudo apt-get install mpich
MPI4PY
  https://www.hackster.io/darthbison/raspberry-pi-cluster-with-mpi-4602cb
TensorFlow
  https://github.com/samjabrahams/tensorflow-on-raspberry-pi

## Slide 15
Pi Cluster Hat – What do you do with it?
Learn distributed processing
Learn parallel programming
  Using Open MPI or other library
Simulate neural networks
  Using TensorFlow or other library
Machine learning
  Using Tensorflow or other library

## Slide 16
Demos
Demo of power controls
  clusterhat on p1
  clusterhat off p3
Demo of networked comms
  ssh pi@p1.local
Demo of distribute
  distribute test.txt
  distribute –c “sudo shutdown –h now”
Demo of parallel computing
  ./uptime.sh
  mpiexec –n 5 --host cluster.local,p1.local,p2.local,p3.local,p4.local python helloworld.py

## Slide 17
Resources
https://clusterhat.com/
https://8086.support/category/23/cluster-hat.html
https://groups.google.com/forum/#!forum/clusterhat
https://www.open-mpi.org/

## Slide 18
Questions?